## Slide 1: Securing IoT Devices on our networks
Eliot Lear
Principal Engineer
31 Oct 2018

## Slide 2: Why is IoT different?

## Slide 3: What’s the scope of the problem?

## Slide 4: Questions that need answering
What is this thing?
What access does it need?
Is it doing what it should be doing?
Who is responsible for it?
What is the device’s identity? Does this particular thing belong on the network?
What type of thing is it?
With which devices is it actually communicating?
Is it behaving as designed?
If something breaks, who should be called?
With which devices should it communicate?
Notes: Eliot – Added AVC to the last bullet point

## Slide 5: Steps needed to get a device to join a network
Out of the box
Device learns which network to join
Provision device to trust network
Provision network to trust device
Operational State

## Slide 6: Design goal choices
Correct network selection
Proof of ownership
Supply chain security

## Slide 7: Basic concept: a voucher
module: ietf-voucher
yang-data voucher-artifact:
+---- voucher
+---- created-on yang:date-and-time
+---- expires-on? yang:date-and-time
+---- assertion enumeration
+---- serial-number string
+---- idevid-issuer? binary
+---- pinned-domain-cert binary
+---- domain-cert-revocation-checks? boolean
+---- nonce? binary
+---- last-renewal-date? yang:date-and-time

## Slide 8: Bootstrapping with wired (ANIMA BRSKI)
Pledge=Device
Registrar=Store of known devices (tied to AAA infrastructure)
MASA=”Manufacturer Authorized Signing Authority”
EST -enrollment over secure transport

## Slide 9: Client gets a certificate via EST

## Slide 10: Getting there with wireless
Use existing management path in the network: EAP
Keep onboarding capabilities in interface “bring up”
Reuse as much as possible
Can do EAP-Success here if we recognize local cert
Can skip BRSKI and go right to enroll if we need to re-enroll

## Slide 11: MASA tests proof of ownership
Thing
MASA
Registrar
1. Label scanned in
2. Normal voucher request
3. Proof of ownership included

## Slide 12: Thing tests proof of ownership
Thing
MASA
Registrar
1. Label scanned in
2. Normal voucher request
3. Proof of ownership included

## Slide 13: No MASA
Thing
Registrar
1. Label scanned in
2. Voucher request
3. Proof of ownership included

## Slide 14: Approaches to onboarding
 | WPS | Simple Serial # | DPP | BRSKI w/ sales integration | BRSKI no sales integration | BRSKI with POP
Correct Network Selection | Yes | Yes | Yes | Yes | No | Yes
Onboard without Internet access | Yes | Yes | Yes | No | No | Yes
Proof of ownership | No | No | No | Yes | Yes** | Yes***
Supply chain security | No | No | No | Yes | Yes*** | Partial
Hands free* | No | No | No | Yes | Yes | No
Well secured | No | Maybe | Yes | Yes | Yes | Yes
Status | Here | Not planned | Std | Partially standardized | Partially standardized | Beginning
Key type | None | Ser # | Asym. | X.509 | X.509 | X.509 + private
Manufacturing complexity | Nvram | Serial# | Public Key + label/BOM | Cert+Back End Integration | Cert | Cert+label/BOM
*Hands free = no label or BOM integration
**Assumes protection of proof of ownership
***Assumes Internet access to enterprise AAA at some point

## Slide 15: Lines of complexity
Certs
Back end sales integration
WPA-2/EAP
Asymmetric Keys
Device
Manufacturing
Deployment Complexity
Labels

## Slide 16: Drafts
draft-ietf-anima-bootstrapping-keyinfra-16 (core draft)
draft-friel-anima-brski-over-802dot11-01 (some options)
draft-lear-eap-teap-brski-01 (BRSKI over EAP)
draft-lear-brski-pop-00 (proof of possession)